3/32” Elgiloy

### Summary

Sphere Specs:

Manufacturer:

| Size | Material | Grade | Gage | Actual |
| --- | --- | --- | --- | --- |
| 3/32 in. | Elgiloy | 100 |  |  |
| Lot No. | Qty | Code | Scan # |

Experiment Dates: 2/23

Labview Time Delay: 9.00

Strobe: 12000 fpm

Scale for tracking program: 161 pixels/cm

Due to the smaller size of the elgiloy spheres, this experiment gave us much trouble.  After a few trials, we noticed that the pictures were being taken fairly high.  To account for this we raised the camera; however, due to the dimensions of the apparatus, we approached a point at which we could not raise the camera any higher.  We then changed the time delay on the second release.  In theory, if the second ball was released sooner, then the collision should occur later.  Getting the collision to occur in the field of view of the camera proved to be difficult.  Strangely enough the collisions did not appear to occur in consistent locations.  After our meeting on that Friday, we arrived at the conclusion that because of the size of the eligiloy spheres, one had in fact gotten stuck in the vent hole at the top of the second release valve.  After we removed the sphere, the experiment continued normally; however, we noticed that the spheres falling into the vent hole was a recurring problem.  Therefore, it is very important to note that this could be a problem when colliding small spheres.

We ran binary collisions with two 3/32” Elgiloy spheres.  The small size of the spheres created problems.  They were hard to handle and hang up on the set-up.  The experiment went relatively smoothly after we figured out our problem; however it was difficult to obtain good α angle’s at certain times.  We began from extreme grazing and moved toward head-on collisions.

We ran a total of 38 collisions, the amount of data reduced because of the smaller size and therefore fewer collisions needed to cover all regimes.  Again, data reduction was not a problem.  There were fewer pictures due to the smaller range of possible colliding surfaces on the spheres.

Two sets of results were obtained.  Partway through this semester it was realized that in one of the data reduction spreadsheets, “coefficient calc-binary.xls”, one value for π was not consistently used.  In some places, 3.14159 was used and in others 3.1415.  To correct this error, since small errors could potentially lead to greater errors, anywhere where a calculation used the value of π, we entered π as a function (i.e. “pi()”) which would use the full value of π in the calculation.  After correcting this error, the data was reduced a second time and no significant changes occurred in resulting values for the properties.  However, there were small changes in the actual numbers for values such as ψ1.

The results did create some scatter.  Overall, because of the small size of the spheres and irregular results we had been receiving, the reduced data was not as bad as it could have been.

First Results

| e | (o | ( |
| --- | --- | --- |
| 0.83 +/-0.02 | 0.30 +/- 0.13 | 0.14 +/-0.01 |

Second Results – with pi correction

| e | (o | ( |
| --- | --- | --- |
| 0.83 +/-0.02 | 0.30 +/- 0.13 | 0.14 +/-0.01 |

The effective e, e’ where e’ = e – (π/2)*(, for elgiloy was about 0.61.  Ideally for our experiments, we’d prefer e’ > 0.7, making elgiloy an unsatisfactory material for our purposes.

#### Images

| Extreme grazing Picture No: 01 | Grazing Picture No: 12 |
| --- | --- |
| Collision Picture No: 29 | Head-on collision Picture No: 38 |

##### Results

“Elgiloy Results.xls”

“Elgiloy Results pi.xls”