3mm Titanium against Glass Plate

### Summary

Sphere Specs:

Manufacturer: Thomson Precision Ball Company, LLC

| Size | Material | Grade | Gage | Actual |
| --- | --- | --- | --- | --- |
| 3 mm | Titanium | 200 | OK | +0.000380 |
| Lot No. | Qty | Code | Scan # |
| 100447988 | 20 Pcs | 12B | TI0118112CXXXMM |

Experiment Dates: 4/26/02

Labview Time Delay: 10.00

Strobe: 12000 fpm

Scale for tracking program: 161 pixels/cm

In continuing with our experiments on Titanium spheres, we ran experiments colliding Titanium spheres against a Glass plate. The setup was almost exactly similar to that of our previous experiment colliding titanium spheres against the 300 Stainless Finished plate. Again we used the vise grip to clamp the stainless steel plate, and adjusted the angle accordingly from 3 degrees when the sphere would collide almost perpendicular to the plate, increasing the angles successively to 79 degrees, where the sphere would almost graze against the plate, in increments of 8 degrees. We took 3 pictures at each angle for a greater range of results. This time, we released the sphere from the top drop tower and we found out it was more flexible to do so.

The experiments were run quite smoothly and efficiently. We reduced the data similarly as we did for the previous 300mm Stainless Finished plate and obtained the following results.

Results

| e | (o | ( |
| --- | --- | --- |
| 0.930 +/- | -0.56+/- 0.41 | 0.086 +/-0.006 |

The effective e we obtained, e’ where e’ = e – (π/2)*(, for Titanium was about 0.795.  Ideally for our experiments, we’d prefer e’ > 0.7, hence for titanium against glass plate would seem to be appropriate.

#### Images

| Head-on collision Picture No: 01 | Less Head-on Picture No: 10 |
| --- | --- |
| Collision Picture No: 22 | Grazing Picture No: 32 |

##### Results

“Titanium Glass Plate Results.xls”